## Slide 1: Resolve in MEM

## Slide 2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F | F | F |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  | Branch resolves in cycle 6 (PC updates end of cycle) Fetch new branch PC in cycle 7
Branches resolve in MEM (Compare in Exec, Branch in Mem), with forwarding enabled and no delay slots Assume stall on branch
Branch Taken case

## Slide 3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F | D | E |  |  |  |  |  |  |  |  |  |  |  |  |  | Assume no branch. Execute speculatively.
add $t5, $t1, $t4 |  |  |  |  | F | D |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  | Branch resolves in cycle 6 (PC updates end of cycle) Fetch new branch PC in cycle 7
Branches resolve in MEM (Compare in Exec, Branch in Mem), with forwarding enabled and no delay slots Assume predict always no branch
Branch Taken case

## Slide 4
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F | F | F | D | E | M | W |  |  |  |  |  |  |  |  |  | Branch resolves in cycle 6 (PC updates end of cycle) No branch. Carry on.
add $t5, $t1, $t4 |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  | 
Branches resolve in MEM (Compare in Exec, Branch in Mem), with forwarding enabled and no delay slots Assume stall on branch
Branch Not Taken case

## Slide 5
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  | Assume no branch. Execute speculatively.
add $t5, $t1, $t4 |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | Branch resolves in cycle 6 (PC updates end of cycle)
add $t3, $t2, $t4 |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | Branch not taken!! I guessed correctly!! Carry on!
tgt: lw $t1, 8($t2) |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  | Just keep executing…
Branches resolve in MEM (Compare in Exec, Branch in Mem), with forwarding enabled and no delay slots Assume predict always no branch
Branch Not Taken case

## Slide 6: Resolve in EXE

## Slide 7
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F | D |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Assume no branch. Execute speculatively.
add $t5, $t1, $t4 |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | Branch resolves in cycle 5 (PC updates end of cycle) Fetch new branch PC in cycle 6
Branches resolve in Exec (Compare in Exec, Branch in Exec), with forwarding enabled and no delay slots Assume predict always no branch
Branch Taken case

## Slide 8
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  | Assume no branch. Execute speculatively.
add $t5, $t1, $t4 |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  | 
Branches resolve in Exec (Compare in Exec, Branch in Exec), with forwarding enabled and no delay slots Assume predict always no branch
Branch Not Taken case

## Slide 9
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Assume no branch. Execute speculatively.
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | Branch fetch in cycle 3, decode in cycle 4, predict always branch and update end of cycle 4, speculatively fetch branch target in cycle 5
Branches resolve in Exec (Compare in Exec, Branch in Exec), with forwarding enabled and no delay slots Assume predict always branch
Branch Taken case
How and when do we know where to branch?
Require Branch Target address calculation in ID stage
Can you do Branch Target address calculation in Fetch?

## Slide 10
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | Assume no branch. Execute speculatively.
add $t5, $t1, $t4 |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  | F |  |  |  | F | D | E | M | W |  |  |  |  |  |  | 
Branches resolve in Exec (Compare in Exec, Branch in Exec), with forwarding enabled and no delay slots Assume predict always branch
Branch Not Taken case