## Slide 1: CS203 – Advanced Computer Architecture
Instruction Set Architectures

## Slide 2: Instruction set architecture (ISA)
The ISA is the interface between software and hardware
Design objectives
Functionality and flexibility for OS and compilers
Implementation efficiency in available technology
Backward compatibility
ISAs are typically designed to last through trends of changes in usage and technology
As time goes by they tend to grow

## Slide 3: Instruction types and opcodes
The opcode of an instruction indicates the operation to perform
Four classes of instructions are considered:
Integer arithmetic/logic instructions
  Add, sub, mult
  Addu, subu,multu
  Or, and, nor, nand
Floating point instructions
  Fadd, fmul, fdiv
  Complex arithmetic
Memory transfer instructions
  Loads and stores
  Test and set, and swap
  May apply to various operand sizes
Control instructions
  Branches are conditional
  Condition may be condition bits (zcvxn)
  Condition may test the value of a register (set by slt instruction)
  Condition may be computed in the branch instruction itself
  Jumps are unconditional with absolute address or address in register
  Jal (jump and link) needed for procedures

## Slide 4: Operands inside the CPU
Include: accumulators, evaluation stacks, registers, and immediate values
Accumulators
  ADDA <mem_address>
  MOVA <mem_address>
Stack
  PUSH <mem_address>
  ADD
  POP <mem_address>
Registers
  LW R1, <memory-address>
  SW R1, <memory_address>
  ADD R2, <memory_address>
  ADD R1,R2,R4
    LOAD/STORE ISAs
  Management by the compiler: register spill/fill
Immediate
  ADDI R1,R2,#5

## Slide 5: Memory Operands
Operand alignment
  Byte-addressable machines
  Operands of size s must be stored at an address that is multiples of s
  Bytes are always aligned
  Half words (16bits) aligned at 0, 2, 4, 6
  Words (32 bits) are aligned at 0, 4, 8, 12, 16,..
  Double words (64 bits) are aligned at 0, 8, 16,...
  Compiler is responsible for aligning operands. Hardware checks and traps if misaligned
  Opcode indicates size (also: tags in memory)
Little vs. Big endian
  Big endian: msb is stored at address xxxxxx00
  Little endian: lsb is stored at address xxxxxx00
  Portability problems, configurable endianness

## Slide 6: Addressing Modes
MODE | EXAMPLE | MEANING
REGISTER | ADD R4,R3 | reg[R4] <- reg[R4] +reg[R3]
IMMEDIATE | ADD R4, #3 | reg[R4] <- reg[R4] + 3
DISPLACEMENT | ADD R4, 100(R1) | reg[R4] <- reg[R4] + Mem[100 + reg[R1]]
REGISTER INDIRECT | ADD R4, (R1) | reg[R4] <- reg[R4] + Mem[reg[R1]]
INDEXED | ADD R3, (R1+R2) | reg[R3] <- reg[R3] + Mem[reg[R1] + reg[R2]]
DIRECT OR ABSOLUTE | ADD R1, (1001) | reg[R1] <- reg[R1] + Mem[1001]
MEMORY INDIRECT | ADD R1, @R3 | reg[R1] <- reg[R1] + Mem[Mem[Reg[3]]]
POST INCREMENT | ADD R1, (R2)+ | ADD R1, (R2) then R2 <- R2+d
PREDECREMENT | ADD R1, -(R2) | R2 <- R2-d then ADD R1, (R2)
PC-RELATIVE | BEZ R1, 100 | if R1==0, PC <- PC+100
PC-RELATIVE | JUMP 200 | Concatenate bits of PC and offset

## Slide 7: Control flow
Types
  conditional branch: beq r1,r2, label
  jump: jum label
  procedure call: call label
  procedure return: return, or, return r4
Conditional branch
  how to specify the condition
    many options
  how to specify the address
    most common: PC relative

## Slide 8: Branch condition
Condition code
  codes: Z, N, V, C (zero, negative, overflow, carry)
  set after any arithmetic or logic operation (ALU)
    add r1, r2, r3
    bc label (branch on carry)
Compare and branch
    beq r1, r2, label (MIPS)
Condition register
  use GPR
    cmp r1, r2, r3
    bnz r1, label
  use condition register
    cmp c2, r1, r3 (PowerPC)

## Slide 9: Instruction format
Options
  Size
    fixed, variable, hybrid
  Field locations
    fixed field: typical of RISC
    multiple fields and/or modifiers
Theoretically any encoding will do. However, watch for code size and decoding complexity.
Decoding is simplified if instruction format is highly predictable

## Slide 10: Exceptions, Traps And Interrupts
Exceptions are rare events triggered by the hardware and forcing the processor to execute a handler
  Includes traps and interrupts
Examples:
  I/O device interrupts
  Operating system calls
  Instruction tracing and breakpoints
  Integer or floating-point arithmetic exceptions
  Page faults
  Misaligned memory accesses
  Memory protection violations
  Undefined instructions
  Hardware failure/alarms
  Power failures
Precise exceptions:
  Synchronized with an instruction
  Exceptions appear in instruction sequence and only the first exception in the pipeline will be architecturally visible
  Save process state at faulting instruction, resume execution after handler
  Often difficult in architectures where multiple instructions execute

## Slide 11: RISC versus CISC
CISC: Complex Inst. Set Computers
  very powerful instructions that model HLL constructs
  micro-programmed control unit
  technology constraints: minimize program footprint in memory
  examples: DEC VAX, Intel x86, IBM

## Slide 12: RISC versus CISC
RISC: Reduced …
  misnamed: Simplified
  load/store ISA, only register operands
  hardwired control unit: fixed field decoding
  designed with compiler in mind …
  examples: MIPS, Sparc, Alpha, PowerPC

## Slide 13: RISC vs. CISC Instruction Set Design
The historical background:
  In first 25 years (1945-70) performance came from both technology and design.
  Design constraints:
    small and slow memories: compact programs are fast.
    small no. of registers: memory operands.
    attempts to bridge the semantic gap: model high level language features in instructions.
    no need for portability: same vendor application, OS and hardware.
    backward compatibility: every new ISA must carry the good and bad of all past ones.
  Result: powerful and complex instructions that are rarely used.

## Slide 14: Frequency - integer CISC instructions
Rank | Instruction | Avg. % executed
1 | load | 22%
2 | conditional branch | 20%
3 | compare | 16%
4 | store | 12%
5 | add | 8%
6 | and | 6%
7 | sub | 5%
8 | move register | 4%
9 | call | 1%
10 | return | 1%
 | Total | 96%
x86 integer code execution
Simple instructions dominate, make the common case fast

## Slide 15: RISC vs. CISC Instruction Set Design
Emergence of RISC
  Very large scale integration (processor on a chip):
    silicon real-estate at a premium. Micro-store occupies about 70% of chip area: replace micro-store with registers ==> load/store ISA.
  Increased difference between CPU and memory speeds.
  Complex instructions were not used by new compilers.
  Software changes:
    reduced reliance on assembly programming, new ISA can be introduced
    standardized vendor independent OS (Unix) became very popular in some market segments (academia and research) – need for portability
Early RISC projects:
  IBM 801 (America), Berkeley SPUR, RISC I and RISC II and Stanford MIPS.

## Slide 16: RISC v/s CISC ISAs
Feature | CISC | RISC
Inst. Length | Variable | Fixed, one word
Inst. Formats | Multiple | Fixed-field decoding
Memory operands | Multiple | Load/store arch.
Addressing mode | Multiple, indirect | One
Inst. Complexity | >1 cycle/inst | 1 cycle/inst
Control unit | μ-programmed | hardwired

## Slide 17: MIPS Instruction Layout

## Slide 18: Compiler Optimizations

## Slide 19: Impact of optimizations
lucas: Fortran90. Performs the Lucas-Lehmer test to check primality of Mersenne numbers 2^p-1, using arbitrary-precision (array-integer) arithmetic.
mcf: C. Large-scale minimum-cost flow problem that we solve with a network simplex algorithm

## Slide 20: And in conclusion …
Modern ISA
  regularity & simplicity more important than power and flexibility
  parallelism (non obstruction of) is key
  beware of additions (to ISAs)! there are no subtractions
Compiler is the customer
  no more handwritten assembly code
Read Appendix A