## Slide 1: CS203 – Advanced Computer Architecture
Pipelining Review

## Slide 2: Pipelining Analogy
Laundry steps:
  Wash
  Dry
  Fold
  Put it away – Closet / Dresser / Neat pile on floor

## Slide 3: Pipelining Analogy
Assuming each step take 1 hour, 4 loads would take 16 hours!
1
2
3
4

## Slide 4: Pipelining Analogy
To speed things up, overlap steps
4 loads of laundry now only takes 7 hours!
1
2
3
4

## Slide 5: Speedup of Pipelining
k stages pipeline, t time per stage, n jobs
Non-pipelined time = n*k*t
Pipelined time = (k+n-1)*t
This is an ideal case:
No job depends on a previous job
All jobs behave exactly the same
Not realistic.

## Slide 6: Simple 5 stage pipeline

## Slide 7: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 8: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 9: Simplified Pipeline
Need registers between stages
  To hold information produced in previous cycle

## Slide 10: Representation of pipeline

## Slide 11: Pipelining
What makes it easy
  all instructions are the same length
  just a few instruction formats
  memory operands appear only in loads and stores
What makes it hard?
  structural hazards: suppose we had only one memory
  control hazards: need to worry about branch instructions
  data hazards: an instruction depends on a previous instruction
What makes it really hard:
  exception handling
  trying to improve performance with out-of-order execution, etc.

## Slide 12: hazards

## Slide 13: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 14: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 15: Structural hazard
two memory accesses in cc4, use Harvard architecture separate data and code memories

## Slide 16: Data hazards

## Slide 17: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3

## Slide 18: Types of data hazards
Read After Write (RAW), true, or dataflow, dependence
    i1: add r1, r2, r3
    i2: add r4, r1, r5
Write After Read (WAR), anti dependence
    i1: add r1, r2, r3
    i2: add r2, r4, r5
Write After Write (WAW), output dependence
    i1: add r1, r2, r3
    i2: add r1, r4, r5

## Slide 19: WAR & WAW
WAR & WAW are name dependencies
  Dependence is on the container’s name not on the value contained.
  Can be eliminated by renaming, static (in software) or dynamic (in hardware)
WAW & WAR cannot occur in the 5-stage MIPS pipeline
  All the writing happens in WB stage, in issue order of instructions
IF
ID
EX
WB
MEM
IF
ID
EX
WB
MEM
IF
ID
EX
WB
MEM

## Slide 20: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 21: Examples of Dependencies

## Slide 22: Control hazards

## Slide 23: Control Hazards
Branch problem:
  branches are resolved in EX stage  2 cycles penalty on taken branches
  Ideal CPI =1. Assuming 2 cycles for all branches and 32% branch instructions  new CPI = 1 + 0.32*2 = 1.64

## Slide 24: Branches are resolved in EX stage
Ex. Branch Not Taken
B = Branch instr. i = instr after Br. j = instr branch to
IF ID EXE MEM WB

## Slide 25: Branches are resolved in EX stage
Ex. Branch Not Taken
B = Branch instr. i = instr after Br. j = instr branch to
IF ID EXE MEM WB
i B
i+1 i B

## Slide 26: Branches are resolved in EX stage
Ex. Branch Taken
B = Branch instr. i = instr after Br. j = instr branch to
IF ID EXE MEM WB

## Slide 27: Branches are resolved in EX stage
Ex. Branch Taken
B = Branch instr. i = instr after Br. j = instr branch to
IF ID EXE MEM WB
i B
j B

## Slide 28: Control Hazards
Branch problem:
  branches are resolved in EX stage  2 cycles penalty on taken branches
  Ideal CPI =1. Assuming 2 cycles for all branches and 32% branch instructions  new CPI = 1 + 0.32*2 = 1.64
Solutions:
  Reduce branch penalty: change the datapath – new adder needed in ID stage.
  Fill branch delay slot(s) with useful instruction(s).
  Predict branch (Taken/Not Taken).
    Static branch prediction: same prediction for every instance of that branch
    Dynamic branch prediction: prediction based on path leading to that branch

## Slide 29: Branches are resolved in ID stage
Ex. Branch Not Taken
B = Branch instr. i = instr after Br. j = instr branch to
IF ID EXE MEM WB

## Slide 30: Branches are resolved in ID stage
Ex. Branch Not Taken
B = Branch instr. i = instr after Br. j = instr branch to
IF ID EXE MEM WB
i B
i+1 i B

## Slide 31: Branches are resolved in ID stage
Ex. Branch Taken
B = Branch instr. i = instr after Br. j = instr branch to
IF ID EXE MEM WB

## Slide 32: Branches are resolved in ID stage
Ex. Branch Taken
B = Branch instr. i = instr after Br. j = instr branch to
IF ID EXE MEM WB
i B
j B

## Slide 33: Filling branch delay slots
Branch delay slot filling
  move a useful instruction into the slot right after the branch, hoping that its execution is necessary.
  Limitations: restrictions on which instructions can be rescheduled, compile time prediction of taken or untaken branches; serious impact on program semantics & future architectures.

## Slide 34: Scheduling Branch Delay Slots
add $1,$2,$3
if $2=0 then
delay slot
A. From before branch
B. From branch target
C. From fall through
add $1,$2,$3
if $1=0 then
delay slot
add $1,$2,$3
if $1=0 then
delay slot
sub $4,$5,$6
sub $4,$5,$6
becomes
becomes
becomes
if $2=0 then
add $1,$2,$3
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
Notes: Limitations on delayed-branch scheduling come from 1) restrictions on the instructions that can be moved/copied into the delay slot and 2) limited ability to predict at compile time whether a branch is likely to be taken or not.
In B and C, the use of $1 prevents the add instruction from being moved to the delay slot
In B the sub may need to be copied because it could be reached by another path. B is preferred when the branch is taken with high probability (such as loop branches

## Slide 35: Branch Prediction
Predict the outcome of a branch in the IF stage
  Idea: doing something is better than waiting around doing nothing
  Gains might outweigh losses
  Heavily researched area in the last 20 years
Fixed branch prediction.
  applied to all branch instructions indiscriminately.
  Predict not-taken (47% actually not taken):
    continue to fetch instruction without stalling;; do not change any state (no register write);
    if branch is taken turn the fetched instruction into no-op, restart fetch at target address: 1 cycle penalty. Assumes branch detection at the ID stage.
  Predict taken (53%): more difficult, must know target before branch is decoded; no advantage in our simple 5-stage pipeline even if we move the branch to ID stage.

## Slide 36: Branch Prediction
Static branch prediction.
  Opcode-based: prediction based on opcode itself and related condition. Examples: MC 88110, PowerPC 601/603.
  Displacement based prediction: if d < 0 (LOOP) predict taken, if d >= 0 predict not taken. Examples: Alpha 21064 (as option), PowerPC 601/603 for regular conditional branches.
  Compiler-directed prediction: compiler sets or clears a predict bit in the instruction itself. Examples: AT&T 9210 Hobbit, PowerPC 601/603 (predict bit reverses opcode or displacement predictions), HP PA 8000 (as option).
Dynamic branch prediction
  Later in this course; tons of it!
  Why is it SO important? For what?