## Slide 1: CS203 – Advanced Computer Architecture
Branch Prediction

## Slide 2: Static Branch Prediction
To reorder code around branches, we need to predict branch statically when compiling
  Always taken / not taken
Can be compiler directed
  Delayed Branch
  Hint bits (branch likely, branch not likely)

## Slide 3: Dynamic Branch Prediction
Why does prediction work?
  Underlying algorithm has regularities
  Data that is being operated on has regularities
  Instruction sequence has redundancies that are artifacts of way that humans/compilers think about problems
Is dynamic branch prediction better than static branch prediction?
  Seems to be
  There are a small number of important branches in programs which have dynamic behavior

## Slide 4: Dynamic Branch Prediction
Branch Prediction Buffer (BPB) accessed with Instruction on I-Fetch
Also called Branch History Table (BHT), Branch Prediction Table (BPT)

## Slide 5: 1-bit Predictor
Each BHT entry is 1-bit
  Bit records last outcome of the branch
  Predicts that next outcome is the same as the last
Loop1: --- --- Loop2: --- --- BEZ R2, Loop2 --- BNEZ R3, Loop1
BEZ always mispredicted twice for every loop
  Once on entry and once on exit

## Slide 6: 2-bit Predictor
Prediction must miss twice before it is changed
2-bit BHT
Also called 2-bit saturating counter
Can be extended to N-bits (typically N=2)

## Slide 7: 2-bit predictor
Loop1: --- --- Loop2: --- --- BEZ R2, Loop2 --- BNEZ R3, Loop1

## Slide 8: BHT Accuracy
Mispredict due to
  Wrong guess for that branch
  Got branch history of wrong branch when index to the table (aliasing)
Example w/ 4k entries:
Integer
Floating Point

## Slide 9: Observations
Misprediction higher for integer programs than floating point programs
Prediction accuracy doesn’t improve beyond 4k entries

## Slide 10: Correlating Predictors
Look at other branches for clues
  if (aa==2) -- branch b1
  …
  if (bb==2) -- branch b2
  …
  if(aa!=bb) { … -- branch b3 – Clearly depends on the results of b1 and b2

## Slide 11: Correlating Predictors
Record m most recently executed branches as taken / not taken and use that pattern to select proper n-bit branch history table
(m,n) predictor
  Record last m branches to select between 2m BHT
  Each BHT has n-bit counters
    Simple 2-bit BHT is a (0,2) predictor
Global Branch Histroy: m-bit shift register
Also called Two Level predictors
  1st level – global, 2nd level - counters

## Slide 12: Correlating Predictors
Example (2,2) predictor
Branch address
2-bits per branch predictor
Prediction
2-bit global branch history
4

## Slide 13: Correlating Predictor Accuracy
With 1k entries, (2,2) performs better than 2-bit predictor with unlimited entries!

## Slide 14: Local Predictor
Previously, Global Branch History captures global behaviors (global predictor)
  Patterns including neighboring branches
Local predictor capture patterns belonging to the branch being predicted
  if (aa==2) -- branch b1
  …
  if (bb==2) -- branch b2
  …
  if(aa!=bb) { … -- branch b3

## Slide 15: Local Predictor
Branch PC
1001010001
1k entries of 2-bit counters
4-bit
16 entries of 10-bit local branch history
10-bit history index

## Slide 16: Local Predictor
Branch PC
1001010001
1k entries of 2-bit counters
4-bit
16 entries of 10-bit local branch history
10-bit
XOR

## Slide 17: Tournament Predictors
Problem: Some branches work well with local predictors, while other branches work well with global predictors
Solution: Use multiple predictors.
  One based on global information, one based on local information.
  Add a selector to pick between predictors
Local
Global
Tournament
MUX

## Slide 18: Tournament Predictor
How to pick between local or global predictor?
Use n-bit saturating counter to choose between predictors

## Slide 19: Tournament Predictor Accuracy
Advantage of tournament predictor is ability to select the right predictor for a particular branch
    Particularly crucial for integer benchmarks.
    A typical tournament predictor will select the global predictor almost 40% of the time for the SPEC integer benchmarks and less than 15% of the time for the SPEC FP benchmarks
Predictor of Alpha 21264
    Similar to Pentium4 and PPC5
  4K 2-bit predictor to select local or global
  Global predictor
    4K entries indexed by history of last 12 branches, each a 2-bit predictor
  Local predictor: two levels
    Top level 1K 10-bit branch history table
    Each entry index into 1K 3-bit saturating counters

## Slide 20: Predictor Accuracy

## Slide 21: Branch Target Buffers (BTB)
Branch target calculation is costly and stalls instruction fetch
BTB enable fetching to begin after IF-stage
BTB cache predicted PC value
BTB
PC
Branch Target

## Slide 22: Branch Target Buffers

## Slide 23: BTB Algorithm
BTB hit predicted taken = 0 cycle delay
BTB hit misprediction = 2 cycle penalty Correct BTB
BTB miss = 1 cycle penalty Add entry to BTB

## Slide 24: BTB Performance
Two things can go wrong
  BTB miss (misfetch)
  Mispredicted a branch (mispredict)
Ex. Suppose for branches, BTB hit rate of 85% and predict accuracy of 90%, misfetch penalty of 2 cycles and mispredict penalty of 5 cycles. What is the average branch penalty?
  2*(15%) + 5*(85%*10%)
Branch prediction and BTB can be used together to perform better prediction

## Slide 25: Summary
Branch Prediction Buffer – 1-bit and 2-bit
Correlating Predictor (Two-level)
  Incorporates global branch information
Tournament Predictor
  Incorporates local branch and global branch info.
  Selector picks between predictors
Branch Target Buffers
  Predicts if instruction is fetch, and branch target address.
  No more stalls on taken branches!