## Slide 1: CS203 – Advanced Computer Architecture
ILP and Speculation

## Slide 2: Speculation
Speculative execution – execute control dependent instructions even when we are not sure if they should be executed
With branch prediction, we speculate on the outcome of the branches and execute the program as if our guesses were correct
  Misprediction – Hardware undo (Rollback and recovery)
In Tomasulo, instructions after the branch can be fetched and issued in-order, but can not execute before the branch is resolved
  Speculation allows them to execute with care
Multi-issue + branch prediction + Tomasulo
  Implemented in a number of processors: PowerPC 603/604/G3/G4, Pentium II/III/4, Alpha 21264, AMD K5/K6/Athlon, MIPS R10k/R12k

## Slide 3: Adding Speculation to Tomasulo
Must separate execution from allowing instruction to finish or “commit”
  This additional step called instruction commit
  When an instruction is no longer speculative, allow it to update the register file or memory
  Requires additional set of buffers to hold results of instructions that have finished execution but have not committed
This reorder buffer (ROB) is also used to pass results among instructions that may be speculated

## Slide 4: Reorder Buffer (ROB)
In Tomasulo’s algorithm, once an instruction writes its result, any subsequently issued instructions will find result in the register file
With speculation, the register file is not updated until the instruction commits
  (we know definitively that the instruction should execute)
Thus, the ROB supplies operands in interval between completion of instruction execution and instruction commit
  ROB is a source of operands for instructions, just as reservation stations (RS) provide operands in Tomasulo’s algorithm
  ROB extends architecture registers like RS

## Slide 5: Reorder Buffer Entry
Each entry in the ROB contains four fields:
  Instruction type
    a branch (has no destination result), a store (has a memory address destination), or a register operation (ALU operation or load, which has register destinations)
  Destination
    Register number (for loads and ALU operations) or memory address (for stores) where the instruction result should be written
  Value
    Value of instruction result until the instruction commits
  Ready
    Indicates that instruction has completed execution, and the value is ready

## Slide 6: Reorder Buffer Operation
Holds instructions in FIFO order, exactly as issued
  When instructions complete, results placed into ROB
    Supplies operands to other instruction between execution complete & commit  more registers like RS
    Tag results with ROB buffer number instead of reservation station
  Instructions commit values at head of ROB placed in registers
As a result, easy to undo speculated instructions on mispredicted branches or on exceptions
Reorder
Buffer
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations
FP Regs
Commit path

## Slide 7: 4 Steps of Speculative Tomasulo Algorithm
Issue—get instruction from FP Op Queue
  If reservation station and reorder buffer slot free, issue instr & send operands & reorder buffer no. for destination (this stage sometimes called “dispatch”)
Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result; when both in reservation station, execute; checks RAW (sometimes called “issue”)
Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting FUs & reorder buffer; mark reservation station available.
Commit—update register with reorder result
  When instr. at head of reorder buffer & result present, update register with result (or store to memory) and remove instr from reorder buffer.
  Mispredicted branch flushes reorder buffer (sometimes called “graduation”)

## Slide 8: Avoiding Memory Hazards
WAW and WAR hazards through memory are eliminated with speculation because actual updating of memory occurs in order, when a store is at head of the ROB, and hence, no earlier loads or stores can still be pending
RAW hazards through memory are maintained by two restrictions:
  not allowing a load to initiate the second step of its execution if any active ROB entry occupied by a store has a Destination field that matches the value of the A field of the load, and
  maintaining the program order for the computation of an effective address of a load with respect to all earlier stores.
These restrictions ensure that any load that accesses a memory location written to by an earlier store cannot perform the memory access until the store has written the data

## Slide 9: Exceptions
Technique for both precise interrupts/exceptions and speculation: in-order completion and in-order commit
  If we speculate and are wrong, need to back up and restart execution to point at which we predicted incorrectly
  This is exactly same as need to do with precise exceptions
Exceptions are handled by not recognizing the exception until instruction that caused it is ready to commit in ROB
  If a speculated instruction raises an exception, the exception is recorded in the ROB
  This is why reorder buffers in all new processors