## Slide 1: CS203 – Advanced Computer Architecture
Tomasulo Algorithm
- Speculative Superscalar

## Slide 2: Tomasulo Example
Loop: LD R2,0(R1)
DADDIU R2,R2,#1
SD R2,0(R1)
DADDIU R1,R1,#8
BNE R2,R3,LOOP
Assumption:
Add/Branch – 1 cycle
Load/Store – 2 cycles
(Addr. Gen & Mem. Access)
*Assume 2-issue superscalar
2 instruction can commit/clock
(2 CDB)
Branch
FP Adder
Memory

## Slide 3
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 |  |  |  |  |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) |  |  |  |  |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 |  |  |  |  |  |  | (R2) = 6
1 | SD R2, 0(R1) |  |  |  |  |  |  | Mem[100] = 6
1 | DADDIU R1, R1, #8 |  |  |  |  |  |  | (R1) = 108
1 | BNE R2, R3, LOOP |  |  |  |  |  |  | 6 ≠ 10
2 | LD R2, 0(R1) |  |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 |  |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  |  | 7 ≠ 10
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 |  |  |  | 
Rob8 |  |  |  | 
Rob7 |  |  |  | 
Rob6 |  |  |  | 
Rob5 |  |  |  | 
Rob4 |  |  |  | 
Rob3 |  |  |  | 
Rob2 |  |  |  | 
Rob1 |  |  |  | 
Busy field not shown here due to space constraint.
If there’s no entry, busy = 0, else busy = 1

## Slide 4
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 | Rob2 | ADD |  | 1 | Rob1 |  | 
Add2 |  |  |  |  |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 |  |  |  |  |  |  | 
Load1 | Rob1 | LD | 100 |  |  |  | 0
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Cycle 1: LD1 – Issue, ADD1a – Issue
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 |  |  |  | 
Rob8 |  |  |  | 
Rob7 |  |  |  | 
Rob6 |  |  |  | 
Rob5 |  |  |  | 
Rob4 |  |  |  | 
Rob3 |  |  |  | 
Rob2 | ADD | R2 |  | 0
Rob1 | LD | R2 |  | 0
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 |  |  |  |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 |  |  |  |  |  | (R2) = 6
1 | SD R2, 0(R1) |  |  |  |  |  |  | Mem[100] = 6
1 | DADDIU R1, R1, #8 |  |  |  |  |  |  | (R1) = 108
1 | BNE R2, R3, LOOP |  |  |  |  |  |  | 6 ≠ 10
2 | LD R2, 0(R1) |  |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 |  |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  |  | 7 ≠ 10

## Slide 5
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 | Rob2 | ADD |  | 1 | Rob1 |  | 
Add2 | Rob4 | ADD | 100 | 8 |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 |  |  |  |  |  |  | 
Load1 | Rob1 | LD | 100 |  |  |  | 100
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Cycle 2: LD1 – Calc. Addr., ADD1a – Wait for R2 (LD1), SD1 – Issue, ADD1b - Issue
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 |  |  |  | 
Rob8 |  |  |  | 
Rob7 |  |  |  | 
Rob6 |  |  |  | 
Rob5 |  |  |  | 
Rob4 | ADD | R1 |  | 0
Rob3 | SD | 0+(R1) | Rob2 | 0
Rob2 | ADD | R2 |  | 0
Rob1 | LD | R2 |  | 0
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 |  |  |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 |  |  |  |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 |  |  |  |  |  | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 |  |  |  |  |  | (R1) = 108
1 | BNE R2, R3, LOOP |  |  |  |  |  |  | 6 ≠ 10
2 | LD R2, 0(R1) |  |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 |  |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  |  | 7 ≠ 10

## Slide 6
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 | Rob2 | ADD |  | 1 | Rob1 |  | 
Add2 | Rob4 | ADD | 100 | 8 |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 | Rob5 | BNE |  | 10 | Rob2 |  | 
Br2 |  |  |  |  |  |  | 
Load1 | Rob1 | LD | 100 |  |  |  | 100
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Cycle 3: LD1 – Load, ADD1a – Wait for R2 (LD1), SD1 – Calc. Addr, ADD1b – Execute, BNE1 - Issue
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 |  |  |  | 
Rob8 |  |  |  | 
Rob7 |  |  |  | 
Rob6 |  |  |  | 
Rob5 | BNE |  |  | 0
Rob4 | ADD | R1 |  | 0
Rob3 | SD | 100 | Rob2 | 0
Rob2 | ADD | R2 |  | 0
Rob1 | LD | R2 |  | 0
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 |  |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 |  |  |  |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  |  |  | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 |  |  |  |  |  | 6 ≠ 10
2 | LD R2, 0(R1) |  |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 |  |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  |  | 7 ≠ 10

## Slide 7
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 | Rob2 | ADD | 5 | 1 |  |  | 
Add2 | Rob4 | ADD | 100 | 8 |  |  | 
Add3 | Rob7 | ADD |  | 1 | Rob6 |  | 
Br1 | Rob5 | BNE |  | 10 | Rob2 |  | 
Br2 |  |  |  |  |  |  | 
Load1 | Rob1 | LD | 100 |  |  |  | 100
Load2 | Rob6 | LD | 108 |  |  |  | 0
Load3 |  |  |  |  |  |  | 
Cycle 4: LD1 – CDB, ADD1a – Wait for R2 (LD1), SD1 – Wait for R2 (ADD1a), ADD1b – CDB, BNE1 – Wait for R2 (ADD1a), LD2 – Issue, ADD2a - Issue
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 |  |  |  | 
Rob8 |  |  |  | 
Rob7 | ADD | R2 |  | 0
Rob6 | LD | R2 |  | 0
Rob5 | BNE |  |  | 0
Rob4 | ADD | R1 | 108 | 1
Rob3 | SD | 100 | Rob2 | 0
Rob2 | ADD | R2 |  | 0
Rob1 | LD | R2 | 5 | 1
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 |  |  |  |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 |  | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 |  |  |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  |  | 7 ≠ 10

## Slide 8
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 | Rob2 | ADD | 5 | 1 |  |  | 
Add2 | Rob9 | ADD | 108 | 8 |  |  | 
Add3 | Rob7 | ADD |  | 1 | Rob6 |  | 
Br1 | Rob5 | BNE |  | 10 | Rob2 |  | 
Br2 |  |  |  |  |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 | Rob6 | LD | 108 |  |  |  | 108
Load3 |  |  |  |  |  |  | 
Cycle 5: LD1 – Commit, ADD1a Execute, SD1 – Wait for R2 (ADD1a), ADD1b – Wait to Commit, BNE1 – Wait for R2 (ADD1a), LD2 – Calc Addr., ADD2a – Wait for R2 (LD2), SD2 – Issue, ADD2b - Issue
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 | ADD | R1 |  | 0
Rob8 | SD | 0+(R1) | Rob7 | 0
Rob7 | ADD | R2 |  | 0
Rob6 | LD | R2 |  | 0
Rob5 | BNE |  |  | 0
Rob4 | ADD | R1 | 108 | 1
Rob3 | SD | 100 | Rob2 | 0
Rob2 | ADD | R2 |  | 0
Rob1 | LD | R2 | 5 | 1
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 | 5 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  |  |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 |  | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 |  |  |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 5 |  |  |  | No Exec. Delay | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  |  | 7 ≠ 10

## Slide 9
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 | Rob2 | ADD | 5 | 1 |  |  | 
Add2 | Rob9 | ADD | 108 | 8 |  |  | 
Add3 | Rob7 | ADD |  | 1 | Rob6 |  | 
Br1 | Rob5 | BNE | 6 | 10 |  |  | 
Br2 | Rob1 | BNE |  | 10 | Rob7 |  | 
Load1 |  |  |  |  |  |  | 
Load2 | Rob6 | LD | 108 |  |  |  | 108
Load3 |  |  |  |  |  |  | 
Cycle 6: ADD1a CDB, SD1 – Wait for R2 (ADD1a), ADD1b – Wait to Commit, BNE1 – Wait for R2 (ADD1a), LD2 – Load Spec., ADD2a – Wait for R2 (LD2), SD2 – Calc. Addr., ADD2b – Execute, BNE2 - Issue
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 | ADD | R1 |  | 0
Rob8 | SD | 108 | Rob7 | 0
Rob7 | ADD | R2 |  | 0
Rob6 | LD | R2 |  | 0
Rob5 | BNE |  |  | 0
Rob4 | ADD | R1 | 108 | 1
Rob3 | SD | 100 | 6 | 1
Rob2 | ADD | R2 | 6 | 1
Rob1 | BNE |  |  | 0
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 | 5 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 |  | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 |  |  |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 5 | 6 |  |  | No Exec. Delay | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 6 |  |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 6 |  |  |  | Exec. Directly | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  |  | Wait for R2 (ADD) | 7 ≠ 10

## Slide 10
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 | Rob9 | ADD | 108 | 8 |  |  | 
Add3 | Rob7 | ADD | 6 | 1 |  |  | 
Br1 | Rob5 | BNE | 6 | 10 |  |  | 
Br2 | Rob1 | BNE |  | 10 | Rob7 |  | 
Load1 |  |  |  |  |  |  | 
Load2 | Rob6 | LD | 108 |  |  |  | 108
Load3 |  |  |  |  |  |  | 
Cycle 7: ADD1a – Commit, SD1 – Commit, ADD1b – Wait to Commit, BNE1 – Exec., LD2 – CDB, ADD2a – Wait for R2 (LD2), SD2 – Wait for R2 (ADD2a), ADD2b – CDB, BNE2 – Wait for R2 (ADD2a)
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 | ADD | R1 | 116 | 1
Rob8 | SD | 108 | Rob7 | 0
Rob7 | ADD | R2 |  | 0
Rob6 | LD | R2 | 6 | 1
Rob5 | BNE |  |  | 1
Rob4 | ADD | R1 | 108 | 1
Rob3 | SD | 100 | 6 | 1
Rob2 | ADD | R2 | 6 | 1
Rob1 | BNE |  |  | 0
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 | 5 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | 7 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | 7 | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 |  | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 5 | 6 | 7 |  | No Exec. Delay | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 6 |  |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 6 |  | 7 |  | Exec. Directly | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  |  | Wait for R2 (ADD) | 7 ≠ 10

## Slide 11
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 | Rob7 | ADD | 6 | 1 |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 | Rob1 | BNE |  | 10 | Rob7 |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Cycle 8: ADD1b –Commit, BNE1 – Commit, LD2 – Wait to Commit, ADD2a – Exec, SD2 – Wait for R2 (ADD2a), ADD2b – Wait to Commit , BNE2 – Wait for R2 (ADD2a)
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 | ADD | R1 | 116 | 1
Rob8 | SD | 108 | Rob7 | 0
Rob7 | ADD | R2 |  | 0
Rob6 | LD | R2 | 6 | 1
Rob5 | BNE |  |  | 1
Rob4 | ADD | R1 | 108 | 1
Rob3 |  |  |  | 
Rob2 |  |  |  | 
Rob1 | BNE |  |  | 0
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 | 5 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | 7 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | 7 | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | 8 | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | 8 | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 5 | 6 | 7 |  | No Exec. Delay | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 | 8 |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 6 |  |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 6 |  | 7 |  | Exec. Directly | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  |  | Wait for R2 (ADD) | 7 ≠ 10

## Slide 12
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 | Rob7 | ADD | 6 | 1 |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 | Rob1 | BNE | 7 | 10 |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Cycle 9: LD2 – Commit, ADD2a – CDB, SD2 – Wait for R2 (ADD2a), ADD2b – Wait to Commit , BNE2 – Wait for R2 (ADD2a)
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 | ADD | R1 | 116 | 1
Rob8 | SD | 108 | 7 | 1
Rob7 | ADD | R2 | 7 | 1
Rob6 | LD | R2 | 6 | 1
Rob5 |  |  |  | 
Rob4 |  |  |  | 
Rob3 |  |  |  | 
Rob2 |  |  |  | 
Rob1 | BNE |  |  | 0
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 | 5 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | 7 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | 7 | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | 8 | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | 8 | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 5 | 6 | 7 | 9 | No Exec. Delay | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 | 8 |  | 9 |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 6 |  |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 6 |  | 7 |  | Exec. Directly | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  |  | Wait for R2 (ADD) | 7 ≠ 10

## Slide 13
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 | Rob1 | BNE | 7 | 10 |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Cycle 10: ADD2a – Commit, SD2 – Commit, ADD2b – Wait to Commit , BNE2 – Exec
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 | ADD | R1 | 116 | 1
Rob8 | SD | 108 | 7 | 1
Rob7 | ADD | R2 | 7 | 1
Rob6 |  |  |  | 
Rob5 |  |  |  | 
Rob4 |  |  |  | 
Rob3 |  |  |  | 
Rob2 |  |  |  | 
Rob1 | BNE |  |  | 1
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 | 5 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | 7 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | 7 | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | 8 | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | 8 | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 5 | 6 | 7 | 9 | No Exec. Delay | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 | 8 |  | 9 | 10 | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 6 |  |  | 10 | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 6 |  | 7 |  | Exec. Directly | (R1) = 116
2 | BNE R2, R3, LOOP | 6 | 10 |  |  |  | Wait for R2 (ADD) | 7 ≠ 10

## Slide 14
 | Tag | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 |  |  |  |  |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Cycle 11: ADD2b – Commit , BNE2 – Commit
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6
 | Type | Dest. | Value | Ready
Rob9 | ADD | R1 | 116 | 1
Rob8 |  |  |  | 
Rob7 |  |  |  | 
Rob6 |  |  |  | 
Rob5 |  |  |  | 
Rob4 |  |  |  | 
Rob3 |  |  |  | 
Rob2 |  |  |  | 
Rob1 | BNE |  |  | 1
Iter | Instruction | Issue | Exec | Mem access | Wrt. CDB | Commit | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 | 5 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | 7 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | 7 | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | 8 | Exec. Directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | 8 | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 5 | 6 | 7 | 9 | No Exec. Delay | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 | 8 |  | 9 | 10 | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 6 |  |  | 10 | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 6 |  | 7 | 11 | Exec. Directly | (R1) = 116
2 | BNE R2, R3, LOOP | 6 | 10 |  |  | 11 | Wait for R2 (ADD) | 7 ≠ 10